## Slide 1: Cloud and Aerosol size distributions and CCN activity
Sara Lance
WFM Pilot Study, Preliminary Observations
Aug 24, 2017

## Slide 2
Aerosol Impacts: Climate (‘Global Dimming’)
Haze blown off the Eastern coast of China, over Bo Hai Bay and the Yellow Sea

## Slide 3: Aerosol Impacts: Climate (Effects on Clouds)
“Indirect Effect” of Aerosols on Climate
More particles that act as “Cloud Condensation Nuclei” = clouds with a higher concentration of droplets

## Slide 4
Notes: Continuum between the aerosol and cloud measurements, since particles do not remain a constant size. Dry aerosol particles grow hygroscopically when exposed to water vapor. At RH < 100% some particles can swell significantly and become haze particles. Above 100% RH, the hygroscopic particles can then ‘activate’ and act as CCN, at which point they grow very quickly through condensation to become cloud droplets, which are typically 10-20 um in diameter.

## Slide 5: Summit Measurement Summary
Day |  | Aerosol | CCN | Clouds | Notes
Aug 13 | Sun | Total Number | Total Number | Tail end of am clouds | DMA broken
Aug 14 | Mon | Total Number | Total Number |  | DMA broken
Aug 15 | Tues | Size distribution | Total Number in am | FSSP measurements down from 6-10am | DMA leaking, FSSP connectivity problem
Aug 16 | Wed | Size distribution | size resolved, Calibration |  | 
Aug 17 | Thurs | Size distribution | size resolved |  | 
Aug 18 | Fri | Size distribution | size resolved |  | 
Aug 19 | Sat | Size distribution | size resolved |  | Long cloud sampling day
Aug 20 | Sun | Size distribution | size resolved |  | 
Aug 21 | Mon | Size distribution | size resolved, Calibration 10-11:30am |  | Hazy. Clear-air comparison with van
Aug 22 | Tues | Size distribution | size resolved |  | 
Aug 23 | Wed | Size distribution | size resolved |  | 

## Slide 11: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 0.4% Supersaturation

## Slide 12: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 0.6% Supersaturation

## Slide 13: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 0.8% Supersaturation

## Slide 14: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 1.0% Supersaturation

## Slide 15: SMCA (Scanning Mobility CCN Analysis)
08/21/2017
Calibration data w/ AS, 1 scan at 0.6% Supersaturation

## Slide 16: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 0.6% Supersaturation

## Slide 17: SMCA (Scanning Mobility CCN Analysis)
08/21/2017
Calibration data w/ AS, 1 scan at 0.4% Supersaturation

## Slide 18: SMCA (Scanning Mobility CCN Analysis)
08/17/2017
Ambient data, averaging over 26 scans at 0.4% Supersaturation

## Slide 19: Size-resolved CCN measurements = information about aerosol chemical composition
Hygroscopicity Parameter (kappa) for ammonium sulfate is ~0.6
For Organics compounds, kappa is typically < 0.2
(Petters and Kreidenweis, 2007)

## Slide 20: German Study Comparing Hygroscopicity Parameter (kappa) at upwind and downwind sites on cloudy and clear-air days
(Henning et al, 2014)
Full Cloud Events
Non-
Cloud
Events